## Slide 1: Sauna WiFi Automation
Randy Pfeifer
Caution! The enclosed information involves wiring and potential re-wiring of electrical equipment which operates at dangerous voltages and currents.
Providing this information is not a suggestion that you the reader are capable of applying it in your individual product or that you have the skills necessary to do so.
Do not attempt to make any of the documented changes to your equipment or implement any of the enclosed designs if you are not fully qualified to do so. Loss of warranty status or risk of injury may be experienced.
If you have any questions whatsoever about the attached material, you wish to consult with or hire an electrical expert to ensure your safety.
While everything in the attached material has been implemented by the author, no warranty of accuracy is expressed or implied.

## Slide 2: Notes
This design utilizes a WiFi Smart switch to activate/idle a sauna heater system.
The sauna heater is internally controlled via a contactor. The contactor must be controllable with a 120V AC signal.
  Some contactors may be wired / operating with 240V AC
  Some of those contactors may be rated for use with 120V AC
  If the heater has a contactor which will operate at 120V AC, this approach will work.
A separate sauna controller has a timer, thermostat and possibly switches for internal lights for the sauna room
  With this approach, the timer is defeated in some fashion. The output of the thermostat controls the contactor in series with the WiFi Smart switch to turn the heater on and off as the temperature sensor dictates.
  Details of timer bypass and switches for lighting are beyond the scope of this analysis and likely unique to any given heater/controller manufacture / model.
Additional information is shown to allow visual display of Sauna status but is optional and unrelated to the use of a WiFi Smart switch to remotely control the sauna heater

## Slide 3: License
Copyright 2024 Randy Pfeifer
Licensed under the Apache License, Version 2.0 (the "License"); you may not use this file except in compliance with the License. You may obtain a copy of the License at
http://www.apache.org/licenses/LICENSE-2.0
Unless required by applicable law or agreed to in writing, software distributed under the License is distributed on an "AS IS" BASIS, WITHOUT WARRANTIES OR CONDITIONS OF ANY KIND, either express or implied. See the License for the specific language governing permissions and limitations under the License.

## Slide 4: Schematic diagram (Insertion of WiFi Smart switch in Contactor path)
Sauna Controller
(in changing room)
WiFi Smart
switch
L1
Thermostat
Heat sensor (in sauna)
Turn-ON – (T)
N
Call for Heat (C)
Contactor
Heater
L2
For simplification of drawing, ground connections not shown
Voltage of all lines are 120V AC relative to Neutral (N)
L1-to-L2 Voltage is 240V AC
Heating
Elements
240 VAC
120 VAC
Optional
Sauna
Status
Signaling
“Alexa, turn on the Sauna”
Many details of heater removed for clarity (e.g., grounding, over temp limit switch, heating element configuration, etc.)

## Slide 5: Sauna Status Signaling (Optional) State Diagram
T = Turn ON,
!T =Turn OFF (not ON)
C = Call for Heat/ Cycle
!C = Not calling for heat
T*C = T AND C
States reflect color of light lit while in a given state
RED
Green
Yellow
!T
T*C
T*C
!C
!T
!T
T
RED
Yellow
Green
Lights
Off
Warming
Up
Ready!
!T

## Slide 6: State Simulation
T
C
State
Red Yellow Green
Red
Once Sauna is up to target temp, Green light stays on even as thermostat cycles on/off
until sauna is shut off by WiFi switch or manually.
Sauna reaches target temp
(Thermostat shuts off heater)
WiFi Switch ON
“Alexa, turn on the Sauna”
120VAC
0VAC
”Alexa, turn off the Sauna”

## Slide 7: Components for Sauna Signaling
quantity | Part number | Description | Price | As of
4 EACH | 46.52.8.120.0040 | FINDER MIN. INDUSTRIAL RELAY DPDT 8A 120V AC | $6.94 each | 9/17/21
4 EACH | 97.02 | FINDER DIN -RAIL/PANEL MOUNT SCREW TERMINAL (BOX | $4.13 each | 9/17/21
https://www.amazon.com/gp/product/B07HGW8N7R/ref=ppx_yo_dt_b_search_asin_title?ie=UTF8&th=1
Components for WiFi Control
Available from many sources
External lights – 120V AC compatible Red, Yellow, Green – or any colors of your choice)
An example: https://www.amazon.com/gp/product/B07FXCGDDX/ref=ppx_yo_dt_b_search_asin_title?ie=UTF8&psc=1

## Slide 8: Relay implementation of Sauna Signaling State machine
4 Relays
  T – activated when signal T arrives - SPDT
  C – activated when signal C arrives - DPDT
  C-Save – Saves the prior state of relay C - DPST
  G-Save – Saves the prior state of relay G - DPDT
SPDT = Single Pole Double Throw
DPDT= Double Pole Double Throw
DPST = Double Pole Single Throw
N
N
SPDT
DPDT
N
DPST
T
C
CS
GS
All relays purchased are DPDT. A subset of connections are used for SPDT and DPST cases.

## Slide 9: Relay Implementation
N
T
L1
T
Gsave2
Gsave1
C2
N
N
C
C1
N
GSave
Csave2
Csave1
Csave
N
C
Subscripts (e.g., Gsave2) refer to which pole in the relay is used
Lights are 120 VAC lights

## Slide 10: Pictures of implementation
Original Controller
F-1T Finlandia
WiFi Switch and panel
covering relays.
Low on wall between changing room and hot room – never hot there.
Controlled by Alexa or manually operating switch.
Finlandia 6KW heater
Relays wired in wall and wired to WiFi switch (T) and heater thermostat (C).
Drives 120VAC to selected light outside.